## Slide 1: Electrolytic Cells
Is a Galvanic Cell forced to operate in reverse
Process is called electrolysis
This occurs if a voltage greater than that produced by the galvanic cell is applied to it
Electron flow is forced to operate in reverse
Reactions in each half cell will be reversed

## Slide 2: Applications of Electrolysis
Electroplating
  Plating of a thin layer of a metal on another metal to prevent corrosion or improve appearance
Extraction of Reactive Metals
  Such as Sodium or Aluminium from their ores
Industrial Production
  Sodium hydroxide, chlorine , hydrogen

## Slide 3: Applications of Electrolysis
Recharging of Secondary Cells
  Car batteries and NiCads
Increasing the thickness of the surface oxide layer of aluminium metal

## Slide 4: Anode and Cathode
OXIDATION always occurs at the ANODE
REDUCTION always occurs at the CATHODE
In electrolytic cell, the polarity is decided by the way the external voltage is applied.

## Slide 5: Anode and Cathode
Positive terminal makes the electrode it is attached to the ANODE, where oxidation occurs
Negative terminal makes the electrode it is attached to the CATHODE, where reduction occurs

## Slide 6: Electroplating
A metal is coated with another to improve
  Appearance
  Durability
  Resistance to Corrosion
Metal to be plated is connected to Negative electrode
Dipped in solution of ions of coating metal

## Slide 7: Electroplating
Examples
  Silver
    Steel cutlery to make it more decorative and to prevent rusting
  Chromium
    Taps, tools and car parts to make them harder
  Tin
    Steel food containers to prevent contaminating food

## Slide 8: Electroplating
Pure chromium
electrode
Solution of Chromium Ions
Object to be
Coated with
Chromium
Anode
Cathode
–
+
Cr(s)  Cr3+ (aq) + 3e-
Cr3+ (aq) + 3e-  Cr(s)

## Slide 9: Electrowinning
Metals in Groups I and II as well as Aluminium are so easily oxidised their ores cannot be reduced by the usual chemical means.
The Halogens are strong oxidants and as such are difficult to obtain as pure gases

## Slide 10: Electrowinning
In an electrolytic cell, reduction always occurs at the negative electrode and oxidation at the positive electrode
Hence these cells can be used to produce metals and the halogens from their ores.

## Slide 11: Electrowinning
Because water is more easily readily reduced than these metal ions and more readily oxidised than the halogens these reactions cannot occur in aqueous solutions
Despite the expense, these elements can only be obtained by using their molten salts as electrolytes in electrolytic cells
Downs Cell is used to produce sodium and chloride

## Slide 12: Downs Cell
Downs Cell is used to produce sodium and chloride
Molten sodium chloride
Mixed with calcium chloride
+
+
–
Chlorine gas
Sodium chloride added
Sodium metal
Carbon ANODE
Cylindrical
Iron
cathode

## Slide 13: Downs Cell
Oxidation Reaction ANODE (–)
  2Cl – (l)  Cl2 (g) + 2e –
Reduction Reaction CATHODE (+)
  Na+(l) + e–  Na (l)
Overall Reaction
  2Cl – (l) + Na+(l)  Cl2 (g) + Na(l)

## Slide 14: Recharging Secondary Cells
The reactions which deliver the energy in secondary cells are reversed when the cells are recharged.
The overall reactions in each cell in a car battery are

## Slide 15: Recharging Secondary Cells
When Discharging
  Pb (s) + PbO2(s) + 2 SO4 2 – (aq) + 4H+ 
  2PbSO4 (s) + 2H2O (l)
When Recharging
  2PbSO4 (s) + 2H2O (l) 
  Pb (s) + PbO2(s) + 2 SO4 2 – (aq) + 4H+

## Slide 16: Car Battery Discharging
ANODE (oxidation)
CATHODE (reduction)
Electron Flow
–
+
Pb
Pb coated
With PbSO4
Negative
electrode
Positive
electrode
Solution of sulphuric acid

## Slide 17: Car Battery Recharging
CATHODE (reduction)
ANODE (oxidation)
Electron Flow
–
+
Pb coated
With PbSO4
Negative
electrode
Positive
electrode
Pb coated
With PbSO4
Solution of sulphuric acid

## Slide 18: Car Battery
Discharging (Galvanic Cell)
  ANODE (Oxidation)
  Pb (s) + 2 SO4 2 – (aq)  2PbSO4 (s) + + 2e –
  CATHODE (Reduction)
  PbO2(s) + 2 SO4 2 (aq) + 4H+ + 2e –  2PbSO4 (s) + 2H2O (l)

## Slide 19: Car Battery
Recharging (Electrolytic Cell)
  CATHODE (Reduction)
  2PbSO4 (s) + + 2e –  Pb (s) + 2 SO4 2 – (aq)
  ANODE (Reduction)
  2PbSO4 (s) + 2H2O (l)  PbO2(s) + 2 SO4 2 (aq) + 4H+ + 2e –