## Slide 1: ETHENE
C
C
H
H
H
H
C2H4
CH2 ==CH2

## Slide 2: Uses for Ethene
Microwave polyethene film
Plastic milk bottles
Large wheeled rubbish bins
Poly Vinyl Chloride
Polystyrene & Copolymers
Ethanol

## Slide 3: Composition of Natural Gas
Mostly methane (CH4)
<10% Ethane
May contain smaller percentage of alkanes like propane, butane and pentane
May contain small amounts of N2, CO2 & H2S

## Slide 4: Composition of Crude Oil
Mainly of alkanes
A large range of alkanes present (CH4 – C70H140 in numerous isomeric forms
Small amounts of organic compounds containing S, N and O atoms

## Slide 5: A Hydrocarbon
A compound that contains CARBON and HYDROGEN atoms only

## Slide 6: Alkanes
Hydrocarbons with all single C – C bonds
Thus are called Saturated Hydrocarbons
General formula CnH2n+2

## Slide 7: An Homologous Series
A series of organic compounds
similar chemical properties
differ by a – CH2 – group from the previous member
Examples
  The Alkanes
  CH4 C2H6 C3H8 C4H10

## Slide 8: Alkenes
Also hydrocarbons
Have at least one double C – C bond
So are Unsaturated hydrocarbons
General Formula is CnH2n

## Slide 9: Saturated versus Unsaturated
Saturated contains all single C – C bonds
Unsaturated contains at least one double or triple C – C bond

## Slide 10: Alkanes Alkenes.
CH4 – Methane
C2H6 – Ethane
C3H8 – Propane
C4H10 – Butane
C5H12 – Pentane
C6H14 – Hexane
C7H16 – Heptane
C8H18 – Octane
C9H20 – Nonane
C10H22 – Decane
C2H4 – Ethene
C3H6 – Propene
C4H8 – Butene
C5H10 – Pentene
C6H12 – Hexene
C7H14 – Heptene
C8H16 – Octene
C9H18 – Nonene
C10H20 – Decene

## Slide 11: Production of ethene from crude oil
Two main steps
  Fractional Distillation
  Cracking

## Slide 12: Fractional Distillation
Separation of components in crude oil
Takes place in a fractionating tower
Oil is separated into several fractions
Each hydrocarbon in a fraction has a similar boiling temperature

## Slide 13: Fractional Distillation
Crude Oil
110°C
150°C
180°C
260°C
340°C
Refinary Gas (C1 – C4)
Gasoline (C5 – C6)
Naptha (C6 – C10)
Kerosene (C10 – C14)
Gas Oil (C14 – C20)
Bitumen (> C20)
heater

## Slide 14: Fractional Distillation
The bigger the hydrocarbon molecule, the higher it’s boiling temperature
Due to the dispersion forces holding the molecules together being larger as the molecule gets larger

## Slide 15: Cracking process
Two types
  Thermal
    Produces unsaturated hydrocarbons such as ethene, used in petrochemical
  Catalytic
    To increase amount of lighter fractions recovered from crude oil

## Slide 16: Thermal Cracking
Typically involves an Alkane being converted to an Alkene
  C2H6(g) C2H4(g) + H2(g) ΔH = +138kJ mol –1
  C3H8(g) C2H4(g) + CH4(g) ΔH = +81kJ mol –1

## Slide 17: Catalytic Cracking
Typically involves a larger molecule being broken into smaller molecules
This cannot involve high temperatures as these molecules would decompose
Zeolite is used as the catalyst
C29H60(g)  C8H18 (g) + C8H18 (g) + C13H26 (g)

## Slide 18: Desulfurisation
Is removal of sulfur compounds from crude oil
Sulfur needs to be removed so as to
  Minimise emissions of SO2
  Prevent poisoning of catalysts
  Manufacture sulfuric acid

## Slide 19: Properties of Ethene
Unsaturated
Non – polar molecule
Insoluble in water (and other polar solvents)
A flammable gas
Participates in Addition reactions
  (test of unsaturation)

## Slide 20: Properties of Ethene
Polymerises to form Polyethene
Very low BP (–104°C)
Double bond makes it very reactive

## Slide 21: Test for Unsaturation.
Dark brown bromine will turn clear
C
C
Br
Br
H
H
H
H
+

## Slide 22: Test for Unsaturation.
Dark brown bromine will turn clear
C
C
Br
Br
H
H
H
H
+

## Slide 23: Test for Unsaturation.
Dark brown bromine will turn clear
C
C
H
H
H
H
Br
Br

## Slide 24: Test for Unsaturation.
Dark brown bromine will turn clear
C
C
C
C
Br
Br
H
H
H
H
H
H
Br
Br
H
H
+

## Slide 25: Production of Ethanol from Ethene
Addition of steam using a catalyst
C2H4 + H2O C2H5OH
H3PO4
Catalyst
300º C
C
C
C
C
H2O
H
H
H
H
H
H
H
OH
H
H
+
H3PO4
Catalyst
300º C

## Slide 26: Production of Ethanol
Fermentation of sugar is still used to make alcoholic beverages – which is ethanol
Ethene method is used for ethanol for industrial purposes like solvents in cosmetics, pharmaceuticals and inks

## Slide 27: Production of Polyethene
A type of addition reaction
n(CH2 ==CH2)
catalyst
H
C
H
H
C
H
H
C
H
H
C
H
– (CH2 – CH2) –
polyethene

## Slide 28: Production of Polystyrene
C
C
H
H
H
Catalyst
n
C
C
H
H
H
(
)n
Styrene
Polystyrene
= benzene

## Slide 29: Production of Polyvinyl Chloride (PVC)
C
C
H
H
H
Catalyst
n
C
C
H
H
H
(
)n
Vinyl Chloride
PolyVinyl Chloride
Cl
Cl